Student name / Grzegorz Gliński	Multiscale modeling / Static recrystallization and MCMicro testing.	Date of submission: / 11.06.2014
Specialization: / IwH	Comments:	Grade:

# 1. Intruduction
In this project, our task was to implement function for simulating static recrystallization process (SRX), use it with previous project (simple grain grown) and compare obtained results with results from computions preformed by MCMicro application running on grid system.
Also, we should write down all troubles approached when using grid and MCMicro application.
# 2. Project implementation
Application wan implemented in C++ and QT library. As base for the project, previous application was used. Additional functionalities implemented:
- MC static recrystallization algorithm (parameters: number of MC steps, nucleation interval in steps).
- Energy distribution: homogeneous (all cells have same energy), heterogeneous (90% energy if nucleon is placed on bouduary, 10% if not), random for each grain (all cells in same grain have same energy)
- Visualization of energy distribution (switching from grains morphology to energy distribution and back)

Main window: Grain morphology view
Main windows: Energy distribution view
# 3. Results
All tests were run on standard PC computer with configuration:
- CPU: Intel(R) Core(TM)2 Quad CPU Q6600 (running at 3.3GHz)
- RAM: 4GB DDR2
- Operating system: Gentoo Linux (kernel version: 3.1.6-gentoo)

Type	Parameters	Execution time
Grain growth	Space size: 100x100, Grains: 10	9.444s
Grain growth	Space size: 200x200, Grains: 10	49.171s
Grain growth	Space size: 400x400, Grains: 20	338.101s
SRX	Space size: 100x100, Iterations: 50, interval: 10 steps	1.561s
SRX	Space size: 200x200, Iterations: 50, interval: 10 steps	6.572s
SRX	Space size: 400x400, Iterations: 50, interval: 10 steps	45.012s

Below some visualized results from application:

Generated grain morphology

Energy distribution: heterogeneous

Energy distribution: random for each grain

Ilustracja 1: Energy distribution: homogeneous
# 4. Registering on PL-Grid and use zeus server to run MCMicro